## Slide 1
Chandra X-ray Observatory
HRC Anomaly on 24 August 2020
Preliminary Findings & Recommended Actions
Chandra Community Briefing, 26 August 2020
HRC Operations Team
D. Patnaude, R. Kraft, P. Nulsen, G. Tremblay, T. Gauron, A. Kenter, G. Austin, J. Chappell

## Slide 2
At the start of Monday morning’s comm pass, HRC limit violations were noted in the +15V and -15V bus voltage monitors.
At the time, the HRC was not observing and was at half voltage (as expected). The selected detector was HRC-I. Shield rates were nominal. The HRC has not observed for the past ~week, and all telemetry prior to the anomaly has been normal.
Timeline of Events
Anomaly occurs at 03:45:54 UTC on August 24
+15 V bus monitor drops to ~+4 V
+-15 V bus monitor drops to ~-2 V
Reading scatter also increases dramatically

## Slide 3
The full event

## Slide 4
Notes: TOM HAS AN EXPLAINER FOR THIS WONKY TOTAL EVENT RATE BEHAVIOR

## Slide 6
2DETART
Detector event rate A
2SHLDART
Shield event rate A

## Slide 9
The anomaly is due to a problem with the +/- 15 V power supply bus on Side A
  A problem in the +15 V bus would also take out the -15 V power supply due to DC-to-DC design
    A problem in the -15 V bus would not cause issues with the +15 V bus
  There could be a fault in the electronics on this bus
    A load fault that is transient in nature (e.g. an SEL). This should clear with a power cycle.
    OR
    A failed component that is dragging down the +15V bus. This would not clear with a power cycle and would require an A/B change somewhere.
    OR
    A latched-up DC-DC converter may clear with power cycle. Otherwise an A / B swap is indicated.
Current Hypotheses

## Slide 10
The HRC team recommends that we attempt a reset of the Side A electronics on the +/- 15 V power supply
  A CAP for this procedure is now written and ready for review. It is straightforward, and has back-out pathways at several steps.
  Pending a successful CAP review today, we are ready to execute it tonight (pending DSN availability).
  The procedure is considered low-risk and reversible. Chances of causing damage to the instrument are very low.
  If a Side A reset does not return voltages to nominal values, we will execute SCS 41 to power off the instrument again and make plans to swap to Side B.
    We have already begun preparing an activity for a swap to Side B
Recommended actions

## Slide 11
Resetting Side A is lower risk than swapping to Side B.
  This is a straightforward path to resumption of science.
Swapping to Side B is a more complicated intervention:
  The work required would be roughly equivalent to re-doing orbital activation
Swapping to Side B carries significantly more risk:
  It requires movement of a physical relay switch that has not moved in 20 years
“Two plans are better than one”
  If our attempt to reset Side A fails, we can then move to “plan B”, and swap to the redundant side.
Attempting to reset Side A first is a low-risk intervention
  The CAP is already developed and ready for CAP review and potential execution tonight
  We will learn more about the state of the instrument, and test possible hypotheses
  We have clean “back-out” pathways at every step in the CAP.
Why is a Side A reset preferred?

## Slide 12: EXTRA SLIDES

## Slide 13
Side B Electronics are identical to Side A

## Slide 14
At Monday morning’s (BOT 9:45am EST) comm pass, HRC limit violations were noted in the +15V and -15V bus voltage monitors
CEA box temp showed caution high violation
HRC was not observing and was at half voltage (as expected). Selected detector was HRC-I. Shield rates were nominal.
HRC has not observed in the past ~week. Telemetry in the last week has looked normal (until today).
Timeline of Events

## Slide 15
At the morning (BOT 9:45am EST) comm pass, HRC limit violations were noted in the +15V and -15V bus voltage monitors
CEA box temp showed caution high violation
HRC was not observing and was at half voltage (as expected). Selected detector was HRC-I. Shield rates were nominal.
HRC has not observed in the past ~week. Telemetry in the last week has looked normal (until today).
Chandra community briefing from the HRC team
ROUGH TIMELINE

## Slide 16
FA6 heater manually commanded off at 10:38 AM local, because the +5V bus was still on (i.e., the HRC was still largely powered-up). Instrument team recommended to turn the heater off.
Around 11:10 AM, SCS 107 and SCS 41 were manually run to safe the instrument. FA6 heater was re-enabled.
Since the morning briefing, the HRC team has been working to analyze the issue and suggest potential next actions.
ACTIONS TAKEN

## Slide 17
HRC telemetry prior to event has been normal.
HRC has not observed in the past week.
Full-resolution Ska data from August 21-24
-15 V Bus Monitor
+15 V Bus Monitor
5 V Bus Monitor

## Slide 18
Full-resolution Ska data from August 21-24
Step change in telemetry at August 24 03:45:54 UTC
-15 V Bus Monitor
+15 V Bus Monitor
Notes: Event at Chandra Time 714627954.9676153660

## Slide 19
+15 V Bus Monitor
-15 V Bus Monitor
Step change in telemetry at August 24 03:45:54 UTC
Notes: Event at Chandra Time 714627954.9676153660

## Slide 20
All voltage monitors
-15 V Bus Monitor
+15 V Bus Monitor
5 V Bus Monitor
24 V Bus Monitor

## Slide 21
CEA Radiator Temperature
Time of event
Notes: Event at Chandra Time 714627954.9676153660

## Slide 22
2DETART (HRC detectors were off)
DETECTOR EVENT RATE A

## Slide 23
2SHLDART
SHIELD EVENT RATE A

## Slide 24
2SHLDBRT
2SHLDART
SHIELD EVENT RATE A

## Slide 25
2TLEVART
TOTAL EVENT RATE
2SHEVART
SHIELD EVENT RATE
2VLEVART
VALID EVENT RATE (ALWAYS ZERO)

## Slide 26
2TLEVART
TOTAL EVENT RATE

## Slide 27
RECOMMENDED ACTIONS
A controlled power-on of the HRC
  We will need to work with the FOT on this
  At this time, we would advise against turning the HRC on simply to activate the shield

## Slide 28
2TLEVART
TOTAL EVENT RATE